## Slide 1: Controller Area Network
Name: Dhrubo Jouti Das Troyee
Student_ID:22663281
Priority and Contention

## Slide 2: CAN key Aspects
What is CAN?
Multi-master bus system
Devices (nodes) can start communication
Why was it developed?
By Bosch in the 1980s
industry standard in vehicles
Used for :
Airbag development
Engine control
abs braking
Importance:
offers seamless device-to-device connection, particularly when sending several messages at once.
Today’s Focus:
How CAN handles priority and contention?

## Slide 3
What is PRIORITY in CAN?
    In the CAN protocol, each message has a unique identifier.
    unique identifier — often a binary or hexadecimal number.
Did you know ???
    The numerical value of a Can message ID actually determines its priority ?
    The lower the value, the higher the priority.

## Slide 4
Example of Priority
Which message will send first????
Let’s say we have 2 message
💡Why this matter ??
ensures that vital functions (engine control, brakes) are always transmitted quickly.
Non- critical messages like temperature display or music updates) waits until its turn.
message | Identifier(Hex) | Binary | Priority
Braking | 0x 100 | 0001 0000 0000 | higher
Door lock | 0x 200 | 0010 0000 0000 | Lower
    As 0x100 is numerically smaller then 0x200
        Lower ID = HIGHER PRIORITY
        wins the bus access first

## Slide 5
What is contention??
KEY POINTS:
  Happens when 2 or more nodes want to transmit (send data) at the same time.
  In most networks, it could d causes collision or delay.
  Can solve this using bitwise comparison of IDs
  Bits are sent to left to right, one at a time .
important Rules:
    In can 0= dominant Bit (WINS).
    1 = Recessive Bit (Loses) .
    During transmission, each node sends its message ID 1 bit at a time.
  How it works?
    Let’s say , Node A,B are 2 devices . If Node A sends 0 , and Node B sends 1
    The 0 wins on the bus, and node B stop transmitting .
    The message with more leading 0s (lower ID) continues, and others need to wait

## Slide 6
Why CAN works so well??
Summery points
    In CAN priority is based on message ID – lower ID = Higher priority.
    Contention is resolved automatically using the ID bits and the dominant/ recessive rule .
  Key benefits :
    Fast
    Collision-free
    Reliable – especially in real time systems like modern Cars.
  This system makes sure critical message always pass though first and making CAN efficient, safe in demanding environment.

## Slide 7
THANK YOU